KingFisher® Flex process with 96DW magnet head and chemagic Viral DNA/RNA Kit for viral DNA or RNA isolation (chemagen)

Note! This is a protocol developed by the user and it has been successfully used for e.g. isolation of Norovirus RNA from stool samples. The protocol has not been validated at Thermo Fisher Scientific.

Sample process

- Fill the plates according to the Table 1. More information about the reagents in the chemagic Viral DNA/RNA Kit user manual, article no. 193, chemagen

| Plate number | Plate type | Plate name | Content | Sample/reagent volume |
| --- | --- | --- | --- | --- |
| 1 | Microtiter DW 96 plate | Lysis_Binding | Stool sample (in PBS) | 200 µl |
|  |  |  | Lysis Buffer 1 | 200 µl |
|  |  |  | Protease | 10 µl |
|  |  |  | Carrier RNA | 4 µl |
| Dispense step, add... |
| 1 |  |  | Magnetic Beads | 30 µl |
|  |  |  | Binding buffer 2 | 600 µl |
| 2 | Microtiter DW 96 plate | Wash 3 | Wash Buffer 3 | 500 µl |
| 3 | Microtiter DW 96 plate | Wash 4 | Wash Buffer 4 | 500 µl |
| 4 | Microtiter DW 96 plate | Wash 5 | Wash Buffer 5 | 550 µl |
| 5 | KingFisher 96 KF plate | Elution | Elution Buffer 6 | 100 µl |
| 6 | KingFisher 96 KF plate | Tip Plate |  |  |

Table 1. Filling the plates for chemagic viral DNA/RNA isolation

- Combine the 96 deep well tip comb and the KingFisher 96 plate. For more detailed instructions, see KingFisher Flex User manual

- Start the “chemagic Viral DNA/RNA Kit” protocol using arrow keys and START button. You can also run the protocol using a computer, for more details see BindIt software user manual

- Load the plates according to the protocol request and press START after every plate to confirm the action. Use KingFisher Flex 96 deep well tip comb and plate for tip loading

Note! Confirm that the plates are placed in correct orientation: A1 well to be pointed to upper right corner of the plate holder in turntable. A1 row of the plate is then always located in the inner circle of the turntable

- The purification protocol will start when the last plate is loaded and START button is pressed.

- Dispense step: After lysis add 30 μl of resuspended Magnetic Beads and 600 μl of Binding Buffer 2 to plate 1. Beads and binding buffer may be premixed before addition to plate 1

- After the purification process is completed the plates are removed according to instructions shown in the instrument screen. Press START after each plate removal to confirm the action

- When the last plate is removed text End of run will appear. Press STOP to complete the run

For more information: www.thermo.com/kingfisher and www.chemagen.com